In January, 1995, a time and frequency distribution system was put
into operation.  A "Site 1Hz" tick is generated by a TRAK master clock
from a 5 MHz signal from the Sigma Tau hydrogen maser standard. 
The tick and also an IRIG time signal is distributed around the
Green Bank site on fiber optics.  A clock offset measurement system
logs offsets between various clocks about every 10 minutes.  Files
listing these offsets are placed in the anonymous ftp area on osiris
under directory "timer".

Clock offset file names are of the form:  YYYY_MM.tdat, one file per month.
Files are updated daily.  The files contain one entry per hour, which is
a median of values recorded during the hour.  Typically this is a median
of 6 measurements.  If a number such as "987654321" appears, there was no
data recorded for that device.  

-----------------------------------------------------
Format of the clock offset tables -  "*.tdat" format:
-----------------------------------------------------
	Columns are labeled:   ST-GPS  ST-SAO   GPS-SAO  GPS-F85  GPS-F20

	where xxx-yyy means  device xxx minus yyy.  
	A positive quantity means the pulse from xxx precedes yyy.

	ST = Sigma Tau maser (= Site 1Hz)

	SAO = SAO maser at 140-ft, corrected for travel time of 12392 ns
		from the 140-ft building to the Interferometer building
		on the optical fiber.
		Note:   ST-SAO is calculated as:  ST-SAO-12392, and
		       GPS-SAO is calculated as: GPS-SAO-12392.

	GPS = DATUM GPS receiver at the Interferometer building.

	F85 = The formatter of the 85-ft USNO VLBA recording system.

	F20 = The formatter of the 20-meter USNO VLBA recording system.


-----------------------------------------------------
Format of the clock offset tables -  "*.ttac" format:
-----------------------------------------------------
	Columns are labeled:   ST-TAC  ST-SAO   TAC-SAO  TAC-F85  TAC-F20

     These data are the same as the *.tdat  files, except that the "TAC" GPS receiver
     is used instead of the old DATUM.  The TAC is Tom Clark's "Totally Accurate
     Clock", based on a Motorola GPS chip.  The TAC tracks 6 satellites at a time,
     and gives a more accurate time than the DATUM, which tracks only one.


-----------------------------------------------------
Format of the clock offset tables -  "*.t0" format:
-----------------------------------------------------
	Table lists time differences with respect to the Site 1Hz (derived
	from the Sigma Tau maser).
	Columns are labeled:  Site1Hz, GPS, OldST, 140ft, VLB85, VLB20, 140Rtn

	Thus column 1 is time difference: Site1Hz minus Site1Hz
	col 2 is Site1Hz minus GPS, and so on.

	OldST is 1 HZ derived from the Sigma Tau maser by the old counter
	that was used with the HP system.

	140ft is 1Hz from the 140ft maser. The cable from the 140-ft to 
	the Interferometer building has about 5.8 microsec delay.

	VLB85 = formatter tick of the 85-ft USNO VLBA data acquisition system.

	VLB20 = formatter tick of the 20-meter USNO VLBA data acquisition system.

	140Rtn = Site1Hz after being sent to the 140-ft and back on fiber.
		This is the round trip delay.


-----------------------------------------------------
Format of the clock offset tables -  "*.t1" format:
-----------------------------------------------------
	Table lists time differences with respect to GPS.  Otherwise all is
	as described for the "*.t0" tables.