## Slide 1
PAF (FLAG)
Best on single dish
High Cost
Single dish application = smaller funding community
Excellent Tsys/h
Excellent survey speed
“stuck” with cryo approach?
HI
Pulsar (need wider BWs)
Star formation (K-PAF)
Trade Space
Warm L-band PAF (depend on better processing-JPL)
Wideband Feeds
Promising emerging technology
Has application to interferometers (ngVLA, FAST) = larger international funding community
Spillover and matched waveguides and LNAs a challenge
RFI a potential issue…but mitigated by improved ADCs and RFI algorithms
Science support
Trade Space
Science support
Pulsar (need wider BWs, esp. for timing)
Astrochemistry
Single pixel vs. multi-pixel

## Slide 2
Trade Space
Science support
Feed horn arrays/ FPA (ARGUS)
More easily scalable than PAFs
Can be scaled up without large R&D investments (LO distribution possible exception).
Bolometer FPA (MUSTANG)
Possible to scale up number of pixels without large investment
Lower temperature operation best way forward, but requires R&D.
Can use kinetic inductance parametric up convertors (KPUPs) to increase multiplexing technology
Possible leverage of ongoing work on NbTiN superconductors and TKIPs (see below).
Trade Space
Science support
5K operation
Cradle of life
Pulsars
Implementation/sensitivity
Cluster science
Star formation (dust)

## Slide 3
DSP and Large Arrays
Take advantage of Moore’s law/better ADCs and the need to periodically replace digital back ends
Could enable 103 to 106 elements up to 100 GHz BW
Trade Space
Science support
Traveling-wave Kinetic Inductance Parametric Amplifiers (TKIPs)
Near quantum-limited performance over an octave of BW
Operates a milli-Kelvin now – possibility to leverage MUSTANG’s cryostat
Researching 5K operation with a gain >15 dB over a bandwidth of 55-175 GHz
Leverages wide BW feed horns
Trade Space
Science support
Pulsars
Supports WB spectrometer
Astrochemistry

## Slide 4
Trade Space
Science support
RFI and DSP
Increase requirement (smallsats, automotive radar…).
Leverages RFI work on other telescopes (ngVLA?) and commercial DSP and ADC developments
Trade Space
Science support
Radar Transmission/Reception
Possibility on monostatic operation ?
Planetary mapping/probing
Planetary protection
SETI