## Slide 1
Report on TianMa Telescope
(Shanghai 65m radio telescope)
Shanghai
Astronomical
Observatory
Liu Qinghui
Tianma telescope team

## Slide 2
No. | Name | Job
1 | Shen zhiqiang | scientist/ team leader
2 | Liu qinghui | technique
3 | Li bin | receiver
4 | Wang junzhi | scientist
5 | Yan zhen | scientist
6 | LI juan | scientist
7 | Fan qingyuan | telescope
8 | Ling quanbao | mechanical
9 | Wang jinqing | telescope
10 | Zhao rongbing | software
11 | Fu li | mechanical
12 | Zhong weiye | receiver
13 | Wang lingling | Time/freq.
14 | Dong jian | software
No. | Name | Job
15 | Wu yajun | terminal
16 | Xia bo | observation
17 | Jiang yongbin | observation
18 | Yu linfeng | observation
19 | Gou wei | observation
20 | Zuo xiuting | observation
21 | Jiang yongchen | observation
22 | Sun yunxia | observation
23 | Chen ying | observation
24 | Guo wen | observation
25 | Lu xuejiang | observation
26 | Chen qiang | observation
27 | Shao jie | observation
28 | He wenting | secretary
29 | Wu fang | secretary
TianMa Telescope Team

## Slide 3
Content
1. Construction and test
2. Radio astronomical observation
3. Applications in deep spacecraft

## Slide 4
Tianma Telescope is a steerable radio telescope with a diameter of 65 m, built during 2009-2013. Tianma Telescope greatly improves the measurement capabilities of Chinese VLBI network and plays an important role in deep space exploration and astronomy researches.
Brief introduction

## Slide 5
Tianma telescope has successful tracked Chinese lunar mission ChangE-2 in 2012, Lunar soft landing mission ChangE-3 in 2013, ChangE-5 flight test mission in 2014 for VLBI orbit determination, and has made "outstanding contributions".
Tianma telescope successfully carries out observations for spectra lines, pulsar and VLBI radio astronomy, and opened to the outside world.
Preliminary results of Tianma telescope

## Slide 6
Active Surface System 0.015mm
自动换馈
8个波段
Six-link parallel adjustment of sub-reflector
0.05mm
Automatic feed-rotating 1min
Seamless welded azimuth track 0.5mm
Tianma Telescope major innovative points

## Slide 7: Automatic feed-rotating mechanism
Completing observation band switching
within 1 min

## Slide 8
Six-link parallel adjustment of sub-reflector
The left- and right-hand circular polarization efficiency of X band before and after adjustment of sub surface position and orientation.
X、Y、Z
Adjustment amount:
A few centimeters
before adjustment
after adjustment

## Slide 9
Active surface system
Actuators: 1104
Range±15mm, accuracy 0.015mm
With active surface system
Without

## Slide 10
Surface accuracy of main reflector
measured by using holographic technique
Elevation
52deg

## Slide 11
Receiving system of Tianma telescope

## Slide 12
S-band（ 2.2-2.4 G ）
X-band（8.2-9.0 G）
C-band（4-8 GHz）
S/X and C-band receivers

## Slide 13
L, K, Q-band receivers developed by SHAO
1.25-1.75 18-26.5 35-50 GHz

## Slide 14
Receiving system
Band | L | S | C | X | Ku | K | Ka | Q
Wavelength | 18&21cm | 13cm | 5&6cm | 3.6cm | 2.2cm | 1.3cm | 9mm | 7mm
Freq(GHz) | 1.25-1.75 | 2.2-2.4 | 4-8 | 8.2-9.0 | 12-18 | 18-26.5 | 30-34 | 35-50
BW(GHz) | 0.50 | 0.20 | 4.00 | 0.80 | 6.00 | 8.50 | 4.00 | 15.00
BW/CF(%) | 33 | 9 | 67 | 9 | 40 | 38 | 13 | 35
T(Sky)(k) | 12 | 12 | 10 | 10 | 12 | 25 | 25 | 26
T(Rx)(K) | 10 | 21 | 10 | 22 | 15 | 35 | 35 | 40
T(Sys)(K) | 26 | 33 | 20 | 32 | 27 | 60 | 60 | 66
Feed Type | Compact | Conical | Conical | Conical | Conical | Compact | Conical | Compact
Efficiency | 55% | 60% | 65% | 55% | 55% | 50% | 50% | 45%
Polarization | Dual Circ | Dual Circ | Dual Circ | Dual Circ | Dual Circ | Dual Circ | Dual Circ | Dual Circ
Refrigerator | 1020 | 1020 | 350 | 1020 | 350 | 408S2 | 408S2 | 1020
Status | Installed | Installed | Installed | Installed | Installed | Installed | Installed | Installed

## Slide 15: Comparison TMRT with other telescopes
 |  | GBT | Effelsberg | Parkes | Lovell | Tianma
L | Freq | 1.15-1.73 | 1.27-1.45, 1.59-1.73 | 1.2-1.8 | 1.25-1.50, 1.55-1.73 | 1.25-1.75
 | SEFD | 10 | 20,19 | 31 | 36,65 | 31
S | Freq | 1.73-2.6 | 2.20-2.30 | 2.2-2.5 | ----- | 2.2-2.4
 | SEFD | 12 | 300 | 25 | ----- | ≥31
C | Freq | 3.95-5.85 | 5.75-6.75 | 4.5-5.1 | 6.0-7.0 | 4.0-8.0
 | SEFD | 10 | 25 | 61 | 80 | 28
X | Freq | 8.00-10.1 | 7.9-9.0 | 8,1-8.7 | ----- | 8.2-9.0
 | SEFD | 15 | 18 | 170 | ----- | ≥38
Note: System Equivalent Flux Density (SEFD):

## Slide 16
Terminals
VLBI
spectra/
pulsar
Time/
freq.
DBBC
PC
IF

## Slide 17
VLBI（CDAS,DBBC）
Spectra line/pulsar（DIBAS）
Terminals

## Slide 18
Content
1. Construction and test
2. Radio astronomical observation
3. Applications in deep spacecraft

## Slide 19: EVN and IVS VLBI observations
Tianma telescope has taken part in EVN VLBI observations at L , C and S/X band since 2015, and sometime was selected as the reference telescope in data processing.
Tianma telescope also took part in EVN e-VLBI observations with a data transfer rate of 1 Gbps.
Tianma telescope took part in IVS conventional observations for 5 times in 2015, and planning for 7 times in 2016.
coordinate | position (mm) | Position error (mm) | velocity (mm/yr) | Velocity error (mm/yr)
X | -2826708649.89 | 7.305 | -31.42 | 5.600
Y | 4679237081.85 | 11.773 | -17.47 | 7.517
Z | 3274667547.20 | 8.408 | -16.80 | 6.114

## Slide 20
East Asia VLBI observations
Tianma telescope successfully participates in VLBI observations with Korea 3 stations and Japan 4 stations at 43 GHz.These results show that Tianma telescope has VLBI observation ability at Q-band.

## Slide 21
Mapping results for pulsar B2334 + 61 and B0458 + 46. The measuring accuracy was improved by about three times.
Tianma-VLBA VLBI observation

## Slide 22: Tianma pulsar observation
The DIBAS pulsar observation modules were finished and installed at Tianma telescope in June 2014. This backend supports four principal pulsar observation modes:
[1] coherent dedispersion search;
[2] incoherent dedispersion search;
[3] coherent online folding;
[4] incoherent dedispersion online folding.

## Slide 23: Pulsar observation
Integrated profiles and phase–time plots of magnetar J1745–2900
A batch of pulsars have been detected at L、S、C and X band, including the pulsar with the shortest rotational period on the northern sky and the magmetar around the Galactic center. One case of strong radio flare of the magmetar PSR J1745-2900 was detected by the TMRT at X-band.

## Slide 24: The pulsar PSR B1133 + 16 multi-frequency integral profiles. The highest frequency (8600 MHz) results were obtained by using Tianma telescope.
Pulsar observation
Tianma

## Slide 25: DIBAS spectra line observation model
Total support 29 observation model
The highest resolution is 20 Hz
The maximum bandwidth is 1.5 GHz

## Slide 26
Detection of long carbon-chain molecules in Serpens South with TMRT (Li et al. 2016, ApJ, 824, 136)
We detect several long carbon-chain molecules, including HC5N, HC7N, HC9N, C6H, C8H, HC3N and its 13C isotopes toward Serpens south 1a with TMRT. We detected some new transitions and resolved some hyperfine components for the first time in the ISM. This is the third molecular cloud detected in HC9N and C8H. The column densities of these long carbon-chain molecules are almost comparable to those in TMC-1, and hence, like Lupus-1A, this source could also be regarded as "TMC-1 like cloud".
C6H
C8H
Friensen et al. 2013
HC7N
HC9N

## Slide 27: Tianma Running time (2015.4-2016.6)
Chart: 
| 2015.4 | 2015.5 | 2015.6 | 2015.7 | 2015.8 | 2015.9 | 2015.10 | 2015.11 | 2015.12 | 2016.1 | 2016.2 | 2016.3 | 2016.4 | 2016.5 | 2016.6
月度总观测时间 | 397 | 621 | 543 | 551 | 380 | 643 | 653 | 480 | 662 | 591 | 446 | 694 | 634 | 431 | 566
单天线 | 49 | 284 | 204 | 330 | 253 | 236 | 315 | 221 | 310 | 419 | 271 | 371 | 324 | 47 | 206
VLBI观测 | 12 | 24 | 107 | 16 | 28 | 58 | 119 | 47 | 31 | 21 | 95 | 153 | 23 | 35 | 68
测试 | 206 | 313 | 147 | 143 | 81 | 269 | 198 | 104 | 119 | 58 | 55 | 165 | 226 | 64 | 222
维护保养 | 130 | 85 | 62 | 18 | 80 | 21 | 108 | 76 | 93 | 25 | 5 | 61 | 285 | 70
Running time (h)
Total single dish VLBI test maintenance

## Slide 28: Tianma telescope is open to researchers

## Slide 29
We built RFI monitoring platform at Tianma telescope.
RFI is strong at L and S band, very little at X and above bands. C band has a little interference
2 4 6 8 10 12GHz

## Slide 30
Content
1. Construction and test
2. Radio astronomical observation
3. Applications in deep spacecraft

## Slide 31
delay
Range/Doppler
VLBI
(Very Long Baseline Interferometer)
Range/
Doppler
VLBI
VLBI for tracking spacecraft
Tianma telescope has successful tracked Chinese lunar mission CE-2, CE-3 and CE-5T1

## Slide 32
VLBI center
Chinese VLBI network
Shanghai 65m/25m
Chinese VLBI network
Beijing 50m
Urumqi 25m
Kunming
40m
FAST500m

## Slide 33
CE-3 Orbit
Launch
2013-12-1 17:31:32
Flying to moon
100×100km, 4 days.
100×15km, 4 days
Softly landing Dec.14
Rover relative position
Same-beam VLBI
4.7days
ΔDOR VLBI

## Slide 34
High-accuracy VLBI
Quasar
quasar
sat
correlation
atmosphere
（5m+fluc）
H-Maser
PLO
～
PLO
～
H-Maser
PLO
～
PLO
～
ionosphere
（2m+fluc）
satellite
instrument
quasar
quasar
sat
sat
5m 5m 5m 5m 5m 5min
Observation mode
Tianma telescope contribution
A substantial increase in observation sensitivity.
A large expansion of choice of the radio source near spacecraft, improve the accuracy of the calibration.
A substantial increase in the success rate of Delta DOR VLBI delay.
The above 3 points significantly improve the accuracy of the VLBI measurement system, to make a significant contribution to the lunar soft landing .

## Slide 35
3
2
1
0
Delay residual ns
Observation code
Chart: 
| 41610 | 41611 | 41612 | 41613 | 41614 | 41615 | 41616 | 41617 | 41618 | 41619 | 41620 | 41621
实时 | 0.8 | 0.8 | 0.5148 | 1.0012 | 0.72667 | 0.65853 | 0.68263 | 0.71603 | 0.62713 | 0.5331 | 0.421 | 0.37717
精修 | 0.8 | 0.9 | 0.45597 | 1.2642 | 0.23273 | 0.27817 | 0.33747 | 0.4759 | 0.70443 | 0.52563 | 0.5598 | 0.519
CE-2 and CE-3 VLBI delay residual
after orbit determination
Orbit determination error (VLBI+Doppler/Range)
Flying to the moon: hundreds meters
Circling the moon: tens meters
Landing site: tens meters
CE-2
CE-3
Delay error 0.67ns
1.77ns

## Slide 36
CE-3 landing site
Position difference measured by SHAO and NASA was less than 50m
 | longitude | latitude | height
NASA | -19.5116 | 44.1214 | -2640.0
SHAO | -19.5124 | 44.1206 | -2632.0
Position | 17m | 24m | 8m
Lander
Rover

## Slide 37
Same-beam VLBI in CE-3 and CE-5
CE-3
BJ
SH
KM
UR
lander
1
τ
2
τ
3
τ
4
τ
rover
Measuring relative position/orbit by using differential phase delay of same-beam VLBI
X-Band
0.1deg
S-Band
0.4 deg
Moon
Return
Orbiter
Lander
Liu 2010
Chinese Sci.
CE-5

## Slide 38
a-b: a little movement，c-d: several meter movement
e-f: several meter movement ，
g-h: make a turn
a
b
c
d
e
f
g
h
Monitor rover movement with a sensitivity of 5 cm
Differential phase delay

## Slide 39
Rover relative position determination
with an accuracy of 1m.
lander
A
B
D
C
E
S1
A
B
C
D
E
north
east
Lander
Rover
m
m
Liu 2014
Radio Sci.

## Slide 40
Tianma telescope team will continue to work in all aspects of radio astronomy, deep space exploration, science research and education,
Welcome to use Tianma telescope