High Performance, Full-Digital Control on the LMT and KVN Telescopes
David R. Smith (MERLAB), alpha@merlab.com
Kamal Souccar (UMass),
David Gale (INAOE),
F. Peter Schloerb (Umass),
David Hughes (INAOE)

---
The LMT/GTM
50m Diameter (MT-M)
1-4mm (0.85mm)
Fully steerable (Az/El)
Mexico at 4,600m
Primary surface in five rings (12, 24, 48, 48, 48 = 180 segments)
Three rings in use
Full-Digital Control

---
LMT Measurements
Main Axis
  Encoders
  Tilt meters
  Pointing observations
M1 Segments
  Laser metrology
  Photogrammetry

---
LMT Measurements
M1 Surface:
  Laser metrology
  Photogrammetry
  Holography (12 GHz, three elevations)
  Out of focus beam maps (incl. M2)
  Temperature sensors (>60)

---
LMT Surface Metrology
Site: Total station to install to <500mm
INAOE: 6 Metrology technicians + analyst
  Three laser trackers
  Photogrammetry camera
  Calibration scale bars, etc.
Segment setting to 20mm
Surface mapping to 100mm

---
Laser tracker El 90° (5 hrs)
Photogrammetry El 90° (1 hr)

---
Holography El 61° (1 hr)
Photogrammetry El 60° (1 hr)

---
LMT Measurements
Subreflector (M2) Surface
  Laser metrology
  Photogrammetry
M2 Relative Position
M2 Absolute Position
  Focus
  Beam Shape
  Laser metrology

---
LMT Actuation
Main Axis
  16 Azimuth Motors (all wheels)
  4 Elevation Motors
M1 Figure
  336 Segment Actuators (32.5m)
  720 Segment Actuators (50m)
M2
  Hexapod

---
LMT Servo System
LMT Servo System

---
Main Axis Control
Trajectory Generator
P-PI with Feedforward
Friction compensation
Future work (when we get access again!)
  State space (even elevation dependent)
  Adaptive
  Look-up table corrections

---
Active Surface Control
Current Implementation
  Elevation look-up table (holography)
  Additional astigmatism correction
    Out of focus (OOF) beam maps
Future work
  Corrections based on temperature sensors
  Largest effects look like focus/astigmatism
    Corrected with focus and OOF checks

---
M2 Position Control
Pointing and collimation
  Position only (tilt is equivalent)
  Elevation look-up
Focus
  Checks during observation

---
LMT Performance
Main axis accuracy:
    Tracking: <0.5” RMS
    Mapping scans: <1” RMS
All-sky pointing accuracy (RMS):
    Az: 3-4”
    El: 6-8” (known hysteresis in encoder mount)
Surface accuracy (all optics): ~80-85mm
    M1: ~60mm
    M2: ~40mm (now being replaced)
    Setting/other: ~40mm
Hexapod accuracy: 20mm pos., 2” tip/tilt

---
KVN Telescopes
KVN Telescopes
Korean VLBI Network (KVN) Telescopes
  Three fully-steerable telescopes in South Korea
    Ulsan
    Yonsei
    Tamna
  21m Az/El design (Antedo)
  2-7mm

---
KVN Challenges
Surfaces and hexapod are conventional
  Measurement by photogrammetry
Main design challenge is fast switching
  High axis rates
  High axis accelerations
  Smooth motions to avoid vibration

---
Fast Switching Requirements
Fast Switching Requirements
2.5° on sky
2.5s on source
2.5s on reference
Total cycle time, T
  Elevation switching: T≤13s
  Azimuth switching:
    El≤60°, T≤13s
    60°<El≤80°, T≤26s

---
Fast Switching
Fast Switching

---
Main Axis Performance Specifications
KVN Main Axis Specifications
Maximum velocity (Az/El): 3°/s
Maximum acceleration (Az/El): 3°/s2
Minimum smooth rate: 1 arcsec/s
On-sky Pointing accuracy: 4 arcsec RMS
Servo pointing goal: 2 arcsec RMS
LRF (Az/El): 2.5 Hz

---
Drive System Hardware
KVN Drive System
Fast slew/slow tracking
  Brushless servo motors
  2 million counts/rev motor feedback
  Manufacturer proved low speed operation
Amplifier issues
  Rate loop performance superior to torque mode performance for this manufacturer

---
KVN System Architecture

---
Controller Algorithm
KVN Controller Algorithm

---
Controller
KVN Controller
DCU Rate Loop is nominally PI... but
  Better than when closed with PI in torque
Full-state optimal estimator to provide state vector
Model-based control on two-mass model for the position loop. Also includes:
  Integrator
  Trajectory generator
  Feed forward control

---
KVN Performance
Usual metrics (estimates):
  Tracking accuracy: <0.5” RMS
  Fast switching
    Elevation: <13s
    Azimuth: depends on elevation angle

---
KVN Fast Switching in Az
Az +2.5° on sky (2.5°/cos(El))
Large motions at high elevation angles
Settling defined as peak error <4 arcsec.
RMS <2 arcsec
Elevation Angle	Cycle Time (s)
15°	12.6
30°	12.0
50°	12.2
70°	13.7
80°	18.0

---
Digital System Advantages
For both LMT and KVN, the digital system provides excellent performance in main axis control
Architecture means we have access:
  Torque, Rate, Position, Trajectory, Astro.
LMT also has an active surface, improving the performance of the primary
It's OK to be jealous...

---
Digital System Advantages
What do we get with the digital system?
  Usual (but improved):
    Astronomical tracking
    Position switching
    Pointing offsets
    Instrument holds
    Raster scanning
New capabilities also emerge

---
Digital System Capabilities
Easier measurements
  Balance
  Controller frequency response
New observing modes
New surface corrections
Design paradigm
Remember: the goal is time on sky

---
New Observing Modes
Time parametric scan patterns
Position parametric scan patterns

---
Time Parametric Scans
2:3 Lissajous
2:(3.02) Lissajous

---
Rotating Time Parametric Scans
2:3 Lissajous
2:(3.02) Lissajous

---
Position Parametric Scans
For Holography maps
  Frequent return to center of the map
Improved approach
  Make radial cuts through the center
  Rotate to a new starting point and repeat
  Problem: Non-uniform time coverage

---
Radial Map Definition
Parametric Scan Map, 1/r velocity profile
  High velocity near map center
  Smooth the transition to limited region
  Time coverage is increasingly uniform as the limited region is smaller

---
Typical Results (Position)

---
Typical Results (Velocity)

---
New Surface Corrections
Standard practice: Check pointing/focus
OOF to measure astigmatic effects
  Additional Zernike's can also be measured
  Time trade-off
  Astigmatism is most important
Immediate active surface correction

---
New Design Paradigm
Fully Digital Main Axis Control
  Improves with higher LRF
Active surface
  Can remove gravity effects
  Dominant residual effects
    Pointing, focus, astigmatism, trefoil
Homology is not only not necessary, it can reduce performance for active telescopes

---
Questions?