## Slide 1: ESA’s Deep Space Antennas
Dr. Peter Droll, ESA
MetConf 19 – 24 Sept. 2016
Green Bank, WV, USA

## Slide 2: Outline
ESA’s Deep Space Antenna Network
Characteristic of the 35m Beam Wave Guide Antennas
Pointing Error Model and Pointing Calibration System
Pointing Performance
Ka-Band Rx-Tx Beam Offset Generation and Performance

## Slide 3: ESA’s Deep Space Antenna Network
DSA1 (New Norcia)
Australia
DSA2 (Cebreros)
Spain
DSA2 (Malargue)
Argentina
Antennas are remote controlled from control centre at ESOC, Germany

## Slide 4: Missions supported by ESA’s 35 m Antennas

## Slide 5: Characteristic of the 35m BWG Antennas
Operational Frequency Bands | Up to 32 GHz, Feeds with cryogenically cooled LNAs (X-Band, Ka-Band)
Uplink | 20 kW Klystron amplifier @ X-Band 500 W klystron amplifier @ Ka-Band
Main reflector surface accuracy | < 0.30 mm RMS @ wind at 45/60km/h
Dynamic pointing accuracy (open loop pointing) to be achieved @ 99.7 % of time | ≤ 5.5 mdeg @ wind 45 / 60 km/h ≤ 6.5 mdeg @ wind 50 / 70 km/h ≤ 20 mdeg @ wind 100 / 120 km/h
Lowest Antenna Eigenfrequency | > 2 Hz

## Slide 6: 35m BWG Antenna I (DSA3)

## Slide 7: 35m BWG Antenna II
X-Rx/X-TX
Ka-Rx
Ka-Tx
Dichroic Mirrors
Mirror M5

## Slide 8: Antenna Servo System
Servo Controller is based on fully digitally implemented Cascade Controller Structure:
  P for position controller
  PI controller for velocity controller
  Identical controller structure for Az and El

## Slide 9: Alignment of panels with theodolite and photogrammetry measurements

## Slide 10: Surface Accuracy – Performance under worst case conditions
Source of surface error | Surface accuracy [mm] RMS |  | 
 | Elevation angle [deg] |  | 
 | 0 | 30 | 90
Panel Manufacturing Panel Alignment Gravity (dead weight) Wind (50/70 km/h) Temperature gradient (dT = 1K) | 0.081 0.089 0.080 0.069 0.138 | 0.081 0.089 0.069 0.110 0.138 | 0.081 0.089 0.023 0.069 0.138
Gravity deformation (adjusted at 45O) Wind load (50/70 km/h) Temperature gradient | 0.118 0.166 0.113 | 0.034 0.176 0.113 | 0.138 0.134 0.113
Total (RSS) | 0.304 | 0.299 | 0.287
Simulation results and measurement results are combined to determine performance under worst case conditions.
Surface Error Budget for Main reflector surface accuracy.

## Slide 11: Block Diagram Antenna Pointing Error Compensation
ACU
SPEM with 10 terms
RF refraction compensation
Radiometer
PCS
SLALib
TMS
Tiltmeter
Weather Station
Sub
Reflector

## Slide 12: Systematic Pointing Error Model
The systematic pointing error model (SPEM) of the ESA DSAs consists of the following 10 terms:

## Slide 13: Pointing Calibration System I
Pointing Calibration System supports pointing measurements in X, K, Ka-Rx and Ka-Tx.
Fully automated scanning of pre-selected radio stars and semi-automated determination of SPEM coefficients.
Powerful graphical user interface
Currently limited to SPEM with 10 coeff.

## Slide 14: Pointing Calibration System II
2 Scanning methods available in PCS:

## Slide 15: Pointing Calibration System III
Distribution of radio star measurements.
Arrows show direction of measured pointing offset.
Measurements cover well the hemisphere
Measurements are input for SPEM coefficient determination
Typically 100 – 300 measurements required for good model

## Slide 16: Pointing Calibration System IV
SPEM has to be determined for each frequency band and polarisation.
For proper determination of SPEM coefficients, full coverage of hemisphere is important.

## Slide 17: Antenna Pointing Performance, MLG1
32 GHz, RHCP
290 measurements over 4 days
Clear sky, cold and dry weather
approx. 80% of measurements better 2.25 mdeg
 | Max. total PE
32 GHz, RHCP, no wind, measured | 3.8 mdeg
32 GHz, RHCP, wind 45/60 km/h, extrapolated | 5.3 mdeg

## Slide 18: Generating Rx-Tx Squint at 32 GHz
Spacecraft in movement generates an offset between RX and the TX beams (RX-TX squint)
Worst case Receive (Rx) – Transmit (Tx) offset for future ESA missions (BepiColombo) ~ 40 mdeg
Beam offset
ψ
Ψ dependent on:
RTLT
Transversal velocity component
DSA3/Ka-band
DSA3/X-band

## Slide 19: RX-TX Beam Offset Generation I
Rx-Tx offset compensation concept: M8/M12 BWG mirrors tilting system

## Slide 20: RX-TX Beam Offset Generation II
Accurate two-axes M8/M12 rotation implemented by linear actuators
Relationship between mirror tilts & beam aberration angles (BA, BA ) given by 16 degrees of freedom
The mirror tilting occurs after SPEM correction to automatically compensate systematic pointing error contributions

## Slide 21: RX-TX Beam Offset Generation III
BWG design intrinsically introduces beam shifts (frequency and polarization dependent) → SPEM compensation based on CRX, CRY coefficients
Design of BWG aims at minimizing differences between the possible configurations
Remaining difference can however not be neglected
Simulated for AZ/EL = 0/0 deg (with dichroics)
Effect modelled by CRX/CRY
3.2 mdeg

## Slide 22: Measuring of Rx-Tx beam offset & Ka-TX gain loss
Ka-Tx steering in open loop to verify:
  Pointing accuracy
  Gain degradation
Ka-Rx is the “zero” pointing reference
Both Ka-TX\x and Ka-Rx in “receive” mode (radiometer)
No simultaneous measurements at Ka-RX/TX

## Slide 23: Rx-Tx beam steering performance I
No commanded offset → pointing error due to systematic effects (polarisation dependency, residual mechanical misalignment) → CRX = 0.54 mdeg, CRY = 0.26 mdeg
Need for more meas. to better
cover full hemisphere

## Slide 24: Rx-Tx beam steering performance II
Commanded offset → anomaly detected as gain increase for certain offset directions (i.e. XEL direction)
Worst case gain loss (black line) is worse than expected → due to meas. uncertainty?

## Slide 25: Rx-Tx beam steering performance III
Commanded offset → systematic residual pointing error vectors in a “vortex” around 0,0
Due to not optimum C-matrix coefficients?
Additional losses due to unexpected large pointing errors → -1.5 dB at 30 mdeg

## Slide 26: Next Step: Optimizing Ka Rx-Tx pointing
Current limitations:
Same coefficients for all combinations Rx (RHC, LHC and TX (RHC, LHC)
Coefficients are based on a symmetric conditions, the different combinations hit however the elliptical mirror NOT in its vertex.
Introduction of “corrections” for each/some coefficient to consider the different combinations
Combination dependent coefficients
Feasible?