## Slide 1: Green Bank Instrumentation circa 2030
Dan Werthimer and 800 CASPER Collaborators
http://casper.berkeley.edu

## Slide 2: Upcoming Nobel Prizes with Radio Instrumentation
Gravitational Wave Detection (pulsar timing)
(eg: this morning’s LIGO announcement)
Black Hole Physics (Event Horizon Telescope…)
How did the First Stars and Galaxies Form ? (EOR)
What causes FRB’s ?
Measure baryon density of universe using FRB’s
B mode polarization CMB
Discover ET

## Slide 3: Radio Telescope Sensitivity doubles every 3.6 years

## Slide 4
Moores Law – Instruments using FPGA’s:
2X per year (1,000,000 over 20 years)
Notes: 41.jpg

## Slide 5
21 lags 300kHz clock discrete transistors
$19,000
1960 – First Radio Astronomy Digital Correlator
Sandy Weinreb

## Slide 6: Correlator processing power
DLB
103
102
10
104
105
106
DXB
70
75
90
85
80
95
2000
05
10
2015
VLA
GFlops
1
DCB
LOFAR
SMA
DAS
EVN/WSRT
107
103
106
109
ALMA
SKA
.
EVLA
source: Arnold van Ardenne

## Slide 7
We’re on the cusp of technological maturity: “ancestor” simulations of 1035 ops or 0.1c galactic exploration

## Slide 8: CASPER Philosophy and Religion Design Observatories with Plan for Exponential Growth in Digital Processing
Digital Backend should be replaced every 5 years (keep software, toss old - buy new hardware)
DSP Part of Operating Costs, not construction costs

## Slide 9: expect (plan for)
100 GHz bandwidth
1000 to 1M antenna arrays
1000 to 1M beams (commensal experiments)
6:1 or 20:1 ? Feeds and receivers
phased array feeds with low Tsys ?
Observatory removes RFI (part of instrument)

## Slide 10: GBO Receivers circa 2025
0.6 to 4 GHz 6:1 22K single beam
4 to 24 GHz 6:1 22K single beam
20 to 120 GHz 6:1 single beam
0.6 to 2 GHz Phased Array Feed 20K 1,000 beams
75 – 115 GHz 800 beam horn array (ultra-argus)

## Slide 11: “Rocket” PAF
Next generation PAF
  “rocket” elements; “edge” elements
Superb matching with LNA
  Key to improved performance
  Noise Temp due to uncooled LNAs
4x5 prototype constructed
  tested as aperture array
  ~15K better than equivalent ASKAP tests
  Tested on Parkes
    Measurements affected by RFI
Design better suited to cooling
   CryoPAF funding proposal
    Full 94 dual-pol array + ASKAP back-end
    Expected Tsys <20K !?

## Slide 12: Parkes UltaWideBand system
Quadridge structure with dielectric spear
0.7—4.0 GHz, Tsys ~22K, SEFD ~35 Jy
First light Aug 2017, commission late 2017
Sampler/digitiser and timing (Back-end)
  4 Gsps (2 GHz bands)
Ethernet switch and GPU cluster
  Installed 2016 & used PAF@Parkes
  Software - collaborators
RFI mitigation built-in – reference antenna
Notes: Noise below 1 GHz and above 3.5 GHz due to mis-matched LNA which will be replaced. New LNAs did not cool and used LNAs designed for 1-3.5 GHz for ATCA.

## Slide 14: Instrument Architectures
Scalable
Upgradeable
Flexible
General and Multi-Purpose
Fault Tolerant

## Slide 15: Simultaneous Digital Backends Piggyback, Commensal, Sky Surveys
Signal Splitter
Pulsar Spectrometer
Baseband Data Recorder
Galactic Spectrometer
Extra Galactic Spectrometer
SETI Spectrometer
Analog Power Splitters
or
Digital Data Splitter

## Slide 16
CASPER General Purpose Architechture
Dynamic Allocation of Resources, need not be FPGA based

## Slide 17: VEGAS/DIBAS Multi-beam Spectrometer + Pulsar Timing/Searching John Ford, Dan Werthimer, David MacMahon, Richard Prestage

## Slide 18: FRB121102 (repeater) Highest Frequency detection (4 – 9 GHz) widest bandwidth (5.4 GHz)

## Slide 19: Coherently dedispersed pulses
Law et al. 2017

## Slide 20: Fast ADC’s 15 Gsps 4 bit Adsantec 26 Gsps 3.5 bit Analog Devices 55 Gsps 8 bit Fujitsu 80 Gsps 8 bit Berkeley 160 Gsps 8 bit Keysight 240 Gsps 8 bit Teledyne Lecroy

## Slide 21: Dual 26 Gsps 3.5 bit ADC and FPGA

## Slide 22: Board Interconnect - Upgradable
Problem: Backplanes are short lived
(S100, Multibus, VME, ISA, EISA, PCI, PCIx, PCIe, PCIe2.0, compactPCI, compactPCIe, ATCA…)
Solution: Use 10, 40 or 100 Gbit/sec Ethernet
Ethernet since 1973 – likely to stay around !

## Slide 24: VCU118 5x100Gbit Ethernet ports

## Slide 25: Casper Commandments
Thou Shalt Share thy Knowledge
Thou Shalt Help thy Neighbor Casperite
Thou Shalt Covet thy Ethernet to Connect Everything
Switches are Free

## Slide 26: CASPER Real-time Signal Processing Instrumentation
Rapid development
Open-source, collaborative
Reusable, platform-independent gateware
Modular, upgradeable hardware
Industry standard ethernet communication
Use switches to interconnect FPGA/GPU/CPU
Low Cost
Notes: 26

## Slide 27: Tutorials
Introduction to Simulink and Roach (blink an LED)
Using 10 Gbit Ethernet
Spectrometer (400MHz, 2k channels)
Correlator (4 input, 400MHz, 1k channels)
Heterogeneous Computing ADCROACHCPU/GPU
Intro to embedding Verilog/VHDL in Simulink
Yellow Block Creation

## Slide 28: Annual CASPER Workshops
morning: talks
afternoon: lab training, tutorials, working groups,
get help designing an instrument….