## Slide 1: Fundamentals of the GBT and Single-Dish Radio Telescopes
Dr. Ron Maddalena
National Radio Astronomy Observatory
Green Bank, WV
March 2016
©Associated Universities, Inc., 2016

## Slide 2: National Radio Astronomy Observatory
National Laboratory
Founded in 1954
Funded by the National Science Foundation

## Slide 3: Telescope Structure and Optics

## Slide 4: Telescope Structure and Optics

## Slide 5: Telescope Structure and Optics
Large 100-m Diameter:
  High Sensitivity
  High Angular Resolution – wavelength / Diameter

## Slide 9: Telescope Structure and Optics

## Slide 10: GBT Telescope Optics
110 m x 100 m of a 208 m parent paraboloid
  Effective diameter: 100 m
  Off axis - Clear/Unblocked Aperture

## Slide 11: Telescope Optics
High Dynamic Range
High Fidelity Images

## Slide 12: Telescope Optics
Blockage
Spillover
Stray Radiation

## Slide 13: Telescope Optics

## Slide 15: Telescope Optics
Prime Focus: Retractable boom
Gregorian Focus: 8-m subreflector - 6-degrees of freedom

## Slide 16: Telescope Optics
Rotating Turret with 8 receiver bays

## Slide 17: Telescope Structure
Fully Steerable
  Elevation Limit: 5°
  Can observe 85% of the entire Celestial Sphere
Slew Rates: Azimuth - 40°/min; Elevation - 20°/min

## Slide 18: National Radio Quiet Zone

## Slide 21: National Radio Quiet Zone

## Slide 23: Atmosphere
Index of Refraction
  Weather (i.e., time) and frequency dependent
  Real Part: Bends the light path
  Imaginary part: Opacity
    http://www.gb.nrao.edu/~rmaddale/Weather/
Winds
  Wind-induced pointing errors
  Safety

## Slide 24
Opacity
  Calibration
  System performance – Tsys
  Observing techniques
  Hardware design
Refraction
  Pointing
  Air Mass
    Calibration
    Interferometer & VLB phase errors
  Aperture phase errors
Cloud Cover
  Continuum performance
  Calibration
Winds
  Pointing
  Safety
Telescope Scheduling
  Proportion of proposals that should be accepted
  Telescope productivity
The Influence of the Atmosphere and Weather at cm- and mm-wavelengths

## Slide 25: Weather Forecasts for Radio Astronomy

## Slide 26: Weather Forecasts for Radio Astronomy

## Slide 28: Telescope Structure

## Slide 29: GBT active surface system
Surface has 2004 panels
  average panel rms: 68 µm
2209 precision actuators

## Slide 30: Surface Panel Actuators
One of 2209 actuators.
Actuators are located under each set of surface panel corners
Actuator Control Room
26,508 control and supply wires terminated in this room

## Slide 31: Finite Element Model Predictions

## Slide 32: Mechanical adjustment of the panels

## Slide 33: Image quality and efficiency

## Slide 34: Image quality, efficiency, resolution

## Slide 35: Image quality and efficiency

## Slide 36: Holography
Notes: If you now image the aperture plane to be this circular aperture here, then the technique of holography makes use of the fact that the far field beam pattern is simply the fourier transform of the aperture plane pattern. For a gaussian illuminated aperture plane with no wavefront errors, the beam pattern is a perfect diffraction pattern. If you measure the beam pattern, perform the inverse fourier transform, then the resulting phase in the aperture plane gives you the wavefront, and hence surface error.

## Slide 37: Holography
Notes: If you now image the aperture plane to be this circular aperture here, then the technique of holography makes use of the fact that the far field beam pattern is simply the fourier transform of the aperture plane pattern. For a gaussian illuminated aperture plane with no wavefront errors, the beam pattern is a perfect diffraction pattern. If you measure the beam pattern, perform the inverse fourier transform, then the resulting phase in the aperture plane gives you the wavefront, and hence surface error.

## Slide 38
Surface accuracy (rms) = 240 µm

## Slide 39: Aperture Efficiency
 = rms surface error

## Slide 40: Telescope Structure
Blind Pointing:
(1 point/focus)
Offset Pointing:
(90 min)
Continuous Tracking:
(30 min)

## Slide 41: Optics
Primary Focus
Subreflector / Gregorian Secondary Focus
Focus tracking model
  Residuals measured and removed by observer.
  Tactics: frequency-dependent
Diffraction (Airy) pattern (Beam & Sidelobes) & surface errors
  Optical efficiency: not 100%
    Users must determine and correct for efficiency
    Source-size, frequency and elevation dependent
  Auto OOF Holography
  Stray radiation
Subreflector nodding

## Slide 42: Receiver Focal Plane & Receiver Feeds
Converts EM wave in free space to an electrical wave in a waveguide or cable.
Mustang (Bolometer)
Reciprocity
Illumination (feed taper 10- to 14 dB)
  Stray Radiation
    Spillover
  Efficiency
Array receivers

## Slide 43: Receivers
Receiver | Operating Range | Status
Prime Focus 1 | 0.29—0.92 GHz | Commissioned
Prime Focus 2 | 0.910—1.23 GHz | Commissioned
L Band | 1.15—1.73 GHz | Commissioned
S Band | 1.73—2.60 GHz | Commissioned
C Band | 4—8.0 GHz | Recently upgraded
X Band | 8—12.0 GHz | Commissioned
Ku Band | 12—15 GHz | Commissioned
K Band Array | 18—27 GHz | Commissioned
Ka Band | 26—40 GHz | Commissioned
Q Band | 40—50 GHz | Commissioned
W Band | 68—92 GHz | Commissioned
Mustang Bolometer | 86—94 GHz | Being upgraded
ARGUS | 80—115 GHz | Being commissioned

## Slide 44: Receiver
Band Names (Horrible jargon)
  P- (0.3 GHz), L-, S-, C-, X-, Ku-, K-, Ka-, Q-, W-band (100 GHz).
Parts of typical ‘coherent’ GBT receiver (not Mustang)
  Calibration chopper (W-band)
  Feed(s)
  Polarizer
  Noise coupler (all but W-band) and noise source
  Cryogenic amplifier
  Other amps, attenuators, & filters (depends upon receiver)
  Polarization Hybrid ( < 8 GHz) or switches
  Mixers and Local Oscillator
  Splitters

## Slide 45: Receiver Room

## Slide 46: Typical Receiver

## Slide 47
Receiver Feeds

## Slide 48: Typical Receiver

## Slide 49: Typical Components
Amplifiers
Mixers
Attenuators
Power Detectors
Synthesizers
Splitters
Couplers
Filters
Switches
Multipliers

## Slide 50: Types of Filters
Edges are smoother than illustrated

## Slide 51: Types of Mixers
f
fIF
fLO
n and m are positive or negative integers, usually 1 or -1
Up Conversion : fIF > f
Down Conversion : fIF < f
Lower Side Band : fLO > f
  - Sense of frequency flips
Upper Side Band : fLO < f
fIF = n*fLO + m*f

## Slide 52: 40-Ft System
Determine values for the first LO for the 40-ft when Observing HI at 1420 MHz

## Slide 56: GBT – Astrid program does all the hard work for you…..
configLine = """
receiver = "Rcvr1_2"
beam = “B1"
obstype = "Spectroscopy"
backend = "Spectrometer"
nwin = 1
restfreq = 1420.4058
deltafreq = 0
bandwidth = 12.5
swmode = "tp"
swtype = "none"
swper = 1.0
swfreq = 0.0, 0.0
tint = 30
vlow = 0
vhigh = 0
vframe = "lsrk"
vdef = "Radio"
noisecal = "lo"
pol = "Linear"
nchan = "low"
spect.levels = 3
"""

## Slide 57: Power Balancing/Leveling and Non-Linearity

## Slide 58: Spectral-line observations
Raw Data
Reduced
Data – High
Quality
Reduced
Data –
Problematic

## Slide 59: Reference observations
Difference a signal observation with a reference observation
Types of reference observations
  Frequency Switching
    In or Out-of-band
  Position Switching
  Beam Switching
    Move Subreflector
    Receiver beam-switch
  Dual-Beam Nodding
    Move telescope
    Move Subreflector

## Slide 60: Model Receiver

## Slide 61: Out-Of-Band Frequency Switching

## Slide 62: On-Off Observing

## Slide 63: Nodding with dual-beam receivers - Telescope motion
Optical aberrations
Difference in spillover/ground pickup
Removes any ‘fast’ gain/bandpass changes
Overhead from moving the telescope. All the time is spent on source

## Slide 64: Nodding with dual-beam receivers - Subreflector motion
Optical aberrations
Difference in spillover/ground pickup
Removes any ‘fast’ gain/bandpass changes
Low overhead. All the time is spent on source

## Slide 65: Intrinsic Power P (Watts) Distance R (meters) Aperture A (sq.m.)
Flux = Power Received/Area
Flux Density (S) = Power Received/Area/bandwidth
Bandwidth (BW)
A “Jansky” is a unit of flux density
Notes: Power P Isotropic radiator; in general power may be directive.

## Slide 66: System Temperature
Radiometer Equation

## Slide 67: 40-Ft System

## Slide 68: System Temperature

## Slide 70: System Temperature

## Slide 71: On-Off Observing
Observe blank sky for 10 sec
Move telescope to object & observe for 10 sec
Move to blank sky & observe for 10 sec
Fire noise diode & observe for 10 sec
Observe blank sky for 10 sec

## Slide 72: Continuum - Point Sources On-Off Observing
On Source
Off Source
Off Source
Diode On
TNoiseDiode=3K

## Slide 73: Source Antenna Temperature

## Slide 74: Continuum - Point Sources On-Off Observing
On Source
Off Source
Off Source
Diode On
TNoiseDiode=3K
TA=6K
TSYS=20K

## Slide 75: Converting TA to Scientifically Useful Values