## Slide 1: Topics in Calibration Part I - Antenna Temperatures
Ron Maddalena
01 April 2026

## Slide 2
J.W.M. Baars, “Measurements of Large Antenna with Cosmic Radio Sources”, IEEE Trans. Antennas Propogat., Vol. AP21, no. 4, pp 461-474, July 1973.
B. Winkel, A Kraus, & U Bach, “Unbiased Flux Calibration Methods for Spectral-Line Radio Observations”, A&A 540, 2012.
M.L. Kutner & B.L. Ulich, “Recommendations for Calibration Of Millimeter-Wavelength Spectral Line Data”, ApJ vol. 250, pp 341-348, Nov 1, 1981.
K. Rohlfs & T.L. Wilson, “Tools of Radio Astronomy”, 4th edition. §1.5, 4.2, 5.5, 6.3, 7.1, 7.2.
“Single Dish Radio Astronomy Techniques and Applications”, 2002.
  P.F. Goldsmith, “Radio Telescopes and Measurements at Radio Wavelengths”, §2.2, 4.2, 5, 6, Appendix.
  P.R. Jewell, “Millimeter Wave Calibration Techniques”, §1, 2, 3.
  R.J. Maddalena, “Reduction and Analysis Techniques”, §4

## Slide 3: Outline
My approach
Spectral line calibration
GBTIDL’s ‘GETxxx’ routines
  Multiple sources of
    Systematic calibration errors
    Bad baseline
  Improper way to average integrations and scans
  How to save millions of $$ of telescope time every year
Two alternative algorithms
  Pluses: Baselines & Calibration
  Minuses: Higher Noise
Determining noise source intensities
  Astronomical observations significantly overestimate Tns
  Hot-Cold load measurements give Tns to better than 1%.

## Slide 4: Scientific Relevant Units
etc.
= Antenna Temperature (K)
= Atmospheric Transparency =
x = Efficiency -- specific for the desired units.

## Slide 5: Using Fractional Errors Simplifies the presentation
Systematic Errors:
etc.
Random Errors:
Δ : Systematic errors
σ : Random errors

## Slide 6: GBTIDL Spectral-Line Algorithm for determing Ta getps, getnod, getsigref, GETFS
Simplified in order to show salient points:
where
: Denotes averaging
Anything in Red : A number
Anything in Black : A one-dimensional array
Subscripts:
ref : Reference observation (off source)
sig : Signal observation (on source)
on : Noise source on
off : Noise source off
One-dimensional arrays (frequencies)
Tns : Assumed value of the noise source in K
P : Output of a spectrometer
Tsys : Total system temperature in K
Basics:

## Slide 7
B. Winkel, A Kraus, & U Bach, “Unbiased Flux Calibration Methods for Spectral-Line Radio Observations”, A&A 540, 2012.
: Antenna temperature (what we want)
: Contribution of hardware
: Contribution from spillover
: Contribution from the CMB
: Contribution from the atmosphere
: Contribution from Noise Source
: Instrumental gain in units of Counts / K when observing your source
: Instrumental gain in units of Counts / K when observing your reference position
Modelling
Produces flat baselines and correctly calibrated only if:
: Constant with time
: Constant with frequency and known to high accuracy =

## Slide 8: If all assumptions are satisfied except for a difference in Tsys

## Slide 9: If all assumptions are satisfied except for a difference in G
;
Over time G will also change shape with frequency.

## Slide 10
Tsys not constant Across The band
G & Tsys not constant Across the Band
B. Winkel, A Kraus, & U Bach, “Unbiased Flux Calibration Methods for Spectral-Line Radio Observations”, A&A 540, 2012.
Basics:
Dinner in Elkins on me for the first person to find and fix the error in the ‘frequency-switched’ section of Winkel, Kraus, & Bach

## Slide 11
Instead of:
Use:
Otherwise, for small :

## Slide 12: In-Band Frequency Switching
Correct Algorithm :
is now the product of the gain before the mixer and after the mixer:
If all assumptions are true, plus is constant with frequency and

## Slide 13: In-Band Frequency Switching
Spectral line appears in both phase 1 and 2
are larger than they would be if line did not exist
Both are higher than correct value
Example: Galactic HI or of gas-rich galaxy whose size > FWHM
; ; Bandwidth = 10 MHz
+5%
GBTIDL does not have the ability for users to specify what channels are to be ignored when calculating .

## Slide 14
increases with and
Thus, usually not good idea
to use a receiver’s ‘High’
noise source

## Slide 15
Example: Typically, line widths are a few times the width by which data are smoothed.
M ~ line width / few x channel width.
Try smoothing ref spectra to a few times M:
N ~ line width / channel width
It’ll be like getting 60% more observing time with probably no ill effects on your data.
GBTIDL:

## Slide 16: Averaging Integrations and Scans
GBTIDL:
Requires same number of integrations in Sig and Ref
Assumes G(f) of the nth integration of Sig and the G(f) of nth integration of Ref are correlated.
Degrades baselines
Non-Gaussian noise
Calibration error
Inte-gration | Psig | Pref | 
1 | 10 | 10 | 1.0
2 | 8 | 12 | 0.67
3 | 12 | 8 | 1.5
4 | 10 | 11 | 0.91
5 | 10 | 9 | 1.11
Sum | 50 | 50 | 
 | 0.0 |  | 0.038
Inte-gration | Psig | Pref | 
1 | 10 | 10 | 1.0
2 | 8 | 12 | 0.67
3 | 12 | 8 | 1.5
4 | 10 | 11 | 0.91
5 | 10 | 9 | 1.11
Sum | 50 | 50 | 
 | 0.0 |  | 0.038
Averaging Scans:
GBTIDL:
UniPOPS:
Recommended:
Weighted averages :

## Slide 17: Calibration error when using GBTIDL’s averaging algorithm

## Slide 18: Baselines produced by GBTIDL’s Averaging Algorithm

## Slide 19: Wasted CPU Cycles
vs
3n additions/subtractions + 3n multiplications/divisions
vs
n additions + 2n multiplications/divisions
vs
n additions + (n+1) divisions
vs
n+m additions + 1divisions

## Slide 20: Alternative Algorithm #1
GBTIDL:
Requires:
: Constant with time
: Constant with frequency and known to high accuracy

## Slide 21: Alternative Algorithm #2
GBTIDL:
Requires
: Constant with time
: Constant with frequency and known to high accuracy

## Slide 22
Algorithm 1
Great when is low
Best when using the ‘High’ noise source.
Smoothing denominator and reference observation helps
Algorithm 2
Better when using the ‘High’ noise source.
Smoothing denominators and reference observation helps
Must resort to polynomial fitting of denominators to recover reasonable noise.
Noise of algorithms 1 and 2 compared to that generated by the GBTIDL algorithm

## Slide 23: What About Tns ? Astronomical Observations
=
Invert Algorithm 1, observe a point source with well known flux density:
Must have accurate values for , and

## Slide 26: What About Tns ? Hot-Cold Load Measurements are far superior
Step 1: Measure
Solve for
Step 2: Measure
Solve for

## Slide 27: Summary
GBTIDL’s ‘GETxxx’ routines
  Best noise
  Bad calibration and baselines
  Showed a better way to average integrations & scans
Alternative algorithms
  Much better baselines & calibration
  Worse noise
Proper smoothing can save giga $$ / year
Tns
  Astronomical measurements will overestimate Tns by many %
  Hot-Cold-Load measurements give Tns to better than 1%

## Slide 28: Preview